## Slide 1: Taxonomy of consistent network update problem
Notes: CAP theorem

## Slide 2: 2-phase commit
Advantages
  Per-packet consistency guaranteed
  No forwarding loop
  Very short scheduling time
  Simple implementation
Disadvantages
  TCAM memory overhead
  Tag overhead (negligible)
  No additional consistence, e.g. Congestion-freedom cant be guaranteed

## Slide 3: SWAN & B4
SWAN suggests to Reserve about 10-30% of link capacity to allow congestion-free updates.
B4 suggests to reduced bandwidth of some or all of the flows during network update which results to fewer packet loss.

## Slide 4: time4
Time4 is an update approach that performs multiple changes at different switches at the same time
This paper presents a class of update scenarios in which prior update methods are suboptimal.
PTP(Precision Time Protocol) can synchronize clocks on the order of 1 microseconds .
TIME4 is an update approach that performs multiple changes at different switches at the same time.
Accuracy: scheduling error affected by
  Clock accuracy
  Execution accuracy

## Slide 5
It is assumed that all links in the networks
Have identical capacity .
Required bandwidth of both flows are
Equal
The paper proved that in a dynamic environment flow swaps are inevitable.

## Slide 6: Model and Definitions
Traffic generates from source s destination d , in a directed graph
Goal is to maximize traffic rate from s to d.
Problem modeled as a game between source and controller.
Theorem 1: source has a strategy that forces the controller to perform a flow swap.
The controller’s goal is to find a forwarding path for all the flows in the system without exceeding the capacity of any of the edges, i.e., to completely avoid loss of packets from the given flows.
The source’s goal is to progressively add flows, without exceeding the network’s capacity, forcing the controller to perform a flow swap

## Slide 7
The network is represented by a directed weighted acyclic graph :G = (V, E, c)
V: set of vertices
E : set of edges
C = set of links capacity
If C=1 of all links : G is referred to as an LFA graph.

## Slide 8
Basic Assumptions :
  Each flow has a fixed bandwidth.
  The controller strives to avoid packet loss
  Flows are unsplit table

## Slide 9: EVALUATION
Environment properties
  71-node testbed
  Each machine is a TIMe4-enabled switch or a host
  A separate machine used as a controller
Performance metrics :
  ∆ : The average time elapsed between two consecutive messages sent by the controller. varies from 1 microseconds to several milliseconds
  : max {installation latency} – min{installation latency}
  δ : max {actual update time – scheduled update time}.
No deep buffering
Performance metric : packet loss
Untimed methods are Previous approached like two-phase and ordered.

## Slide 10: Time4 vs other approaches
Hybrid approaches

## Slide 11: Untimed approaches
Notes: پکت لاس با افزایش تعداد سوییچ ها زیاد نمیشود.

## Slide 12: A hybrid approach